## Slide 1
Physics Informed Neural Network for UAV State Estimation
Nafis Mohammad Nayeem, Dr. Imraan A Faruque, Dr. Martin Hagan

## Slide 2
Introduction
Why PINN was chosen?
Physics-Informed Neural Networks combine data-driven learning with known physical models (PDEs/ODEs)
System dynamics are embedded directly into the training loss via physics residuals
Results in estimates that:
  Conform to physical laws by design
  Require less data than black-box models
  Provide a flexible, mesh-free framework for forward and inverse problems
PINNs act as physics-regularized state estimators, enabling robust and data-efficient UAV state awareness under noisy, GPS-denied, and partially observed conditions.
Big picture: Research on State estimation comparison
Extended Kalman Filter (EKF)
Invariant EKF
Physics-Informed Neural Network (PINN)
Journal is to be submitted to: Proc IMechE Part G (Journal of Aerospace Engineering)

## Slide 3
Motivation and Objective
Why this matters (Aerospace relevance)
Noisy / GPS-denied environments
  Indoor flight, enemy jamming, Mars-like missions
  PINNs rely on fundamental motion equations + minimal IMU data
  Physics regularization limits drift when measurements degrade
Swarm coordination
  Each UAV runs a local PINN estimator
  Shared physics constraints (formation, collision avoidance) enhance cooperative estimation
How it is used here (UAV state estimation)
Simulation-based data generation
  12 UAV states simulated using kinematics and dynamics equations
  Gaussian noise added to mimic imperfect sensors
PINN estimator
  Neural network approximates the UAV state trajectory
  Physics loss enforces flight-dynamics equations
  Data loss enforces consistency with noisy sensor measurements

## Slide 4
Data Generation
UAV dynamics
Kinematics + Dynamics Equations
Control → Forces & Moments
True States
Ground truth (only available in simulation)
Models sensor imperfections
Noisy States
PINN Learning
While enforcing physics as soft-constraint
Gaussian Noise Injection
Stored as training data

## Slide 5
PINN Architecture
PINN estimation is closer to batch smoothing than EKF-style point-wise filtering.

## Slide 6
PINN Loss Function
Neural Network Approximation
A function Xθ(t) parameterized by neural network weight and biases θ. This function approximates the UAV’s state x(t).
Residual of Dynamics
Physics residual was computed by plugging Xθ(t) into the UAV’s differential equations. Any deviation from zero becomes a penalty in the loss function.
Noisy measurements of x(t) were taken from simulation and penalized the deviations from Xθ(t).
Loss Function
Data Loss:
Loss function consists of both data loss and physics loss.
There are other ways to define the error. Here are some examples.
For the purpose of this study, I have chosen MSE, as my error function. It has two components. First one refers the data mismatch and second one for physics mismatch.

## Slide 7
PINN Implementation Steps
Flowchart: PINN-Based Fixed-wing State Estimation

## Slide 8
Working Flow Comparison
Initialization
Model-based Prediction
Measurement-based Correction
EKF
Initialization
Model-based Prediction
Measurement-based Correction
Invariant EKF
Time, Initial x0,, Input u feed into model
Trained PINN Model
Estimated 9 States (Position, Orientation, Body velocity)
PINN

## Slide 9
Hyperparameters
Hyperparameters | Option explored | Option selected
Learning Rate | 0.015 | 0.015
Epochs | 1000-5000 in thousand increment | 5000
Batch Size | 256,512,1024 | 256
Hidden Layers | 4,6,8 | 4
Optimizer | Adam | Adam and L-BFGS-B
Activation Function | Relu, sigmoid, tanh | tanh
Batch Normalization | ON/OFF | ON
Number of Neurons per layer | 50,100,200 | 100
Key points to consider
Data Normalization
Usage of optimizer according to the need
Physics informed learning needs careful lambda hyperparameter choice
Bayesian Optimization can be considered for hyperparameter tuning

## Slide 10
Two Stage Optimization Strategy
Why two stages?
PINN loss is non-convex and stiff (data + physics terms)
A single optimizer is insufficient for both exploration and fine convergence
Stage 1: Adam (Coarse Training)
Used for initial training / early convergence
First-order optimizer (gradient-only)
Adaptive learning rate per parameter (momentum + RMSProp)
Robust to noisy gradients and sparse / irregular collocation points
Quickly drives the solution toward a good region of parameter space
Stage 2: L-BFGS-B (Fine Tuning)
Applied after Adam converges
Uses second-order curvature information (approximate inverse Hessian)
Refines the solution to high accuracy
Enforces parameter bounds when needed
Adam: fast exploration L-BFGS-B: precise refinement
Initialize network parameters
↓
Stage 1: Adam Optimizer
• Fast exploration of parameter space
• Handles noisy gradients
• Stabilizes competing data & physics losses
↓
Switch optimizer (warm start)
↓
Stage 2: L-BFGS-B Optimizer
• Uses curvature information
• Sharpens convergence
• Enforces physics precision
↓
Final PINN state estimate

## Slide 11
Optimizer Choice
Aspect | Adam | L-BFGS-B
Optimization type | First-order | Quasi-Newton
Information used | Gradient only | Gradient + curvature
Primary role | Global exploration | Local refinement
Behavior in PINNs | Stabilizes early training | Enforces physics precision
Sensitivity to noise | Low | Higher
Convergence speed | Fast (early) | Fast (near optimum)
Constraint handling | Not native | Box constraints supported
When used | Beginning of training | End of training

## Slide 12
Error in Training
A PINN may satisfy the governing equations well while still fitting measurements poorly.
Loss imbalance Physics term over-weighted → data fit sacrificed
Noisy / inconsistent data Network trusts clean physics over corrupted measurements
Limited network capacity Physics captured, data variations underfit
Collocation dominance Too many physics points, too few data points
Optimization stiffness Physics gradients dominate, data gradients vanish
Scaling mismatch Physics and data losses on different numerical scales

## Slide 13
TRAINING PROTOCOL
State-space coverage progressively
Motivation
Model
Data
PINN
Results
Sensor-conditioned PINN observer for UAV state estimation
18
Fig. 5. Training phase portraits across selected state pairs.
SEVEN CURRICULUM PHASES
• 1: straight
• 2: + doublet
• 3: + chirp
• 4: + circle
• 5: + helical circle
• 6: + rich multi-sine
• 7: + figure-eight
Phase k loss schedule:
λ_e = min(1, (e+1)/75)
Each phase:
350 Adam epochs → restore best val → L-BFGS-B fine tuning
Notes: Explain the curriculum idea: the network learns easy dynamics first and then sees increasingly complex coupled maneuvers. The phase portraits visually justify coverage.

## Slide 14
Unseen TURN result: dynamics-learning rollout vs EKF/IEKF
Results
15
Comparison of sensor-conditioned and dynamics-learning PINNs for fixed-wing UAV state estimation
15/20
Dynamics-learning rollout is red dashed; EKF is blue dash-dot; IEKF is orange dotted. Subplot titles report rollout RMSE.

## Slide 15
09
Sensor Conditioned PINN architecture figure
This slide replaces the earlier inconsistent architecture image while preserving the same high-level visual structure.
Sensor-conditioned PINN observer | corrected slide deck
09 / 20
Key correction: the model has one trainable state head; the measurement branch is analytic, and the output state includes V_wx,V_wy,V_wz instead of p,q,r.

## Slide 16
Unseen TURN result: sensor-conditioned PINN states
Results
Comparison of sensor-conditioned and dynamics-learning PINNs for fixed-wing UAV state estimation
13/20
Direct PINN estimates are plotted in red against simulator truth in black. Position channels dominate the visible error; wind channels remain small.

## Slide 17
DATA + DIAGNOSTICS
Empirical local observability diagnostic supports state identifiability
Motivation
Model
Data
PINN
Results
Sensor-conditioned PINN observer for UAV state estimation
13
Fig. 6. Finite-difference observability rank for all training maneuvers and the held-out turn.
Finite-difference linearization:
A = ∂f_o/∂x, H = ∂h/∂x
A_d = I + T_s A
Stacked local observability matrix:
O = [ H; H A_d; H A_d²; …; H A_dⁿ⁻¹ ]
Diagnostic criterion:
rank(O) = 12 for the reduced 12-state observer model
Interpretation: the diagnostic is local and numerical; it does not prove global observability, but it indicates that the implemented measurement map is informative enough along the sampled trajectories.
Notes: This diagnostic helps justify the observer setup. Emphasize local, empirical, finite-difference rank—not a formal global proof.

## Slide 18
Direct PINN-to-PINN comparison by state
Comparison
17
Comparison of sensor-conditioned and dynamics-learning PINNs for fixed-wing UAV state estimation
17/20

## Slide 19
Conclusion
Effect of physics weighting (λ)
Moderate λ balances data fitting and physics consistency
Higher λ improves trajectory consistency when data are heavily noise-corrupted
Main conclusions
PINNs successfully reconstruct multiple UAV states without explicit noise modeling
Embedding equations of motion acts as a continuous regularizer
Improved fidelity for unobserved or weakly observed states
Robust performance under noisy sensor conditions

## Slide 20
Next steps
Close
20
Comparison of sensor-conditioned and dynamics-learning PINNs for fixed-wing UAV state estimation
20/20
Conclusion
The two PINN codes solve complementary tasks. The dynamics-learning PINN is stronger for temporal state propagation; the sensor-conditioned PINN is stronger for measurement-conditioned wind and velocity reconstruction.
1. Best current use
Use the dynamics-learning model for rollout-aware process correction, especially where temporal consistency dominates.
2. Best current use
Use sensor conditioning for algebraic measurement consistency, wind recovery, and direct state reconstruction from noisy sensor channels.
3. Next architecture
Build a hybrid: sensor-conditioned transition correction inside a recursive filter with uncertainty and rollout training.
Recommended next experiment: train a recurrent sensor-conditioned transition PINN with measurement updates at every step, compare against EKF/IEKF using the exact saved RMSE arrays, and add ablations for Fourier features, rollout horizon, and physics weights.

## Slide 21
Limitations and Future Study
Observed limitations
Reduced accuracy during highly nonlinear transient maneuvers
Sensitivity to collocation point distribution
Computational cost limits the high fidelity data collection
Assumes the knowledge of system’s governing equation
Future direction
Incorporate model uncertainty and real flight data
Online / streaming PINN formulations
Extend from 9-state to full 12-state estimation
Toward hybrid comparisons with EKF and Invariant EKF
Limitations | Further Improvement
Simulation based synthetic data | Real life data
Static Data | Online stream of data
Collocation point | High number of data point
9 states estimation | 12 states estimation

## Slide 22
Thank You for Your Patience
Questions and Answers